## Slide 1: HABITAT FOR HUMANITY TINY HOME AFFORDABLE HOUSING SITE DESIGN IN FLAGSTAFF, ARIZONA
CENE 486 CAPSTONE PRESENTATION
APRIL 26th, 2019
ANNA KURN
MICHAEL BULRISS
DAVID BORJA
ABDULRAHIM ABDULLAH

## Slide 2: PROJECT UNDERSTANDING
Purpose
  Development of 50 Tiny Homes to provide affordable housing solutions for teachers in Flagstaff
  Preliminary site design with grading and drainage, roads and gutters, utility layout, and preliminary cost estimate
Client: Dr. Steve Mead
  Joint Venture with Habitat for Humanity and Flagstaff Unified School District
Technical Advisor: Stephen Irwin
  Shepard-Wesnitzer Inc.

## Slide 3: LOCATION
Figure 1: Project Location for Habitat for Humanity Affordable Housing development in Flagstaff, Arizona. [1]
Flagstaff, Arizona
NAU Campus
Project Location
I-40

## Slide 4: LOCATION
Figure 2: Project Location for Habitat for Humanity Affordable Housing development in Flagstaff, Arizona. [1]
Flagstaff, Arizona
NAU Campus
Project Location
Sinagua Middle School
East Butler Avenue

## Slide 5: PROJECT SCOPE
Preliminary Site Visit and Assessment
Road, Curb, and Gutter Design
Grading and Drainage Design
Utility Layout and Coordination
Conceptual Plan Set
Preliminary Cost Estimate for Development

## Slide 6: PROJECT LIMITATIONS
Challenges:
  Site Topography
  Communal Parking Lot / ADA Compliance
Exclusions:
  Survey and Tree Survey
  Geotechnical Analysis
  Traffic Impact Analysis
  Structural Engineering/Retaining wall designs
Figure 3: Photo of Project Site Location from Sparrow Ave. [1]

## Slide 7: PROJECT IMPACTS
Environmental Impacts
  Loss of Trees
  Large amounts of earthwork
  Transportation of Import and Export materials
Economic Impacts
  Provides Affordable housing for teachers
  Grants likely needed to subsidize proposed development
Social Impacts
  New development in a neighborhood
  Children play in the area
  Retention of teachers in the Flagstaff Community

## Slide 8: TINY HOME DESIGN
Designed by local architect Karl Eberhard
Home Dimensions: 27’ x 14’ for Studios
Additional One Bedroom Units to add 14’ x 14’
Figure 4-6: Renderings for Tiny Home Designs by Karl Eberhard for Project [2].

## Slide 9: SITE DESIGN CRITERIA
Maximize the number of units that have solar panel access to south-side sun
Reduce number of trees to be removed by arranging homes in existing open/flat areas
Reduce amount of cut/fill required by utilizing existing topography
Provide a park area space on the property available by walking access
Figure 7: Tiny Home by Karl Eberhard as basis of design [2]

## Slide 10: CONFORMANCE WITH CODES
City of Flagstaff Zoning Code 10-50.110.080 Bungalow Court Building Types
  One parking space per unit, 3-9 units per lot
Affordable Housing Incentives
  Resource Protection Standards
  Landscaping Standards Reduction of 10%
  Adjustment of Building Form Standards
Figure 8: Bungalow Court Building Type [4]

## Slide 11: FINAL SITE DESIGN
Total Number of Units: 50
Total Number of Parking Stalls: 51
Number of ADA Accessible Units: 6
Number of ADA Accessible Parking Stalls: 3
Figure 9: Final Site Design for Homes for Teachers development in Flagstaff, Arizona. [1]

## Slide 12: ROAD DESIGN ASSEMBLY
Road Type: Residential Local
Design Speed: 20 mph
Max Grade: 10% with 2% tie-in points
Horizontal Curvature Min: 100’
Lane Width: 8.5 Feet
Curb and Gutter Width: 2 Feet
Sidewalk Width: 5 Feet
Cut and Fill Slopes: 2:1
AC: 3 Inches
ABC: 6 Inches
Sub-base: 4 Inches
Figure 10: COF Detail 10-09-038 for Residential Local Road [4]

## Slide 13: FINAL ROAD DESIGN
Existing Grade
Proposed Road
10% Grade = Driving Factor of Site Design
Figure 11: Final Road Design Plan and Profile for Main Road in Development [4]

## Slide 14: GRADING
Earthwork Volumes (Cubic Yards) | 
Total Cut | 4,562
Total Fill | 6,073
Figure 12: Final Grading Design Plan for Homes for Teachers Development [4]
Table 1: Earthwork Volumes for Homes for Teachers Development

## Slide 15: GRADING
Optimal Building Pads:
ADA accessible units
Concrete sidewalks following slope requirements
Utilizes existing topography
Figure 13: Enlarged Grading Design Plan for Homes for Teachers Development [4]
Figure 12: Final Grading Design Plan for Homes for Teachers Development [4]

## Slide 16: GRADING
Challenges in Design:
Units lower than road elevation
Steps required for access
Larger stem walls on houses and routing of runoff required
Figure 14: Enlarged Grading Design Plan for Homes for Teachers Development [4]
Figure 12: Final Grading Design Plan for Homes for Teachers Development [4]

## Slide 17: DRAINAGE
Figure 14: Final Drainage Design Plan for Homes for Teachers Development [4]

## Slide 18: DRAINAGE
Rational Method utilized
Time of Concentration: 5 minutes
Rip Rap Open Channels used to create flow paths down to LID Basins
Grouted Rip Rap used where velocities approach 18 feet per second
Flow down street gutter will tie into existing infrastructure on Sparrow Ave
Table 2: Drainage Plan Impervious Areas and LID Analysis for Basin Storage

## Slide 19: UTILITY LAYOUT
Figure 16 : Utility Layout Alternative 1 with Spanning Sewer Connection Lines[7]

## Slide 20: UTILITY DETAILS
Figure 16 : Utility Layout Alternative 1 with Spanning Sewer Connection Lines[7]
Fire Flow Requirement: 1,500 GPM
8” PVC Water Main
8” PVC SDR35 Sanitary Sewer Main
48” Manhole Diameter

## Slide 21
Figure 16 : Utility Layout Alternative 1 with Spanning Sewer Connection Lines[7]
Street Tie In
UTILITY LAYOUT

## Slide 22: UTILITY LAYOUT - ALTERNATIVE
Figure 17 : Utility Layout Alternative 2 Lift Station Sewer [4]
Figure 17 : Utility Layout Alternative 2 Lift Station Sewer [4]
Alternative 2:
Packaged Lift Station

## Slide 23: Utility Trench Layout
Water connections at existing pressurized water mains
Minimum space of 12” required between water and gas in horizontal and vertical directions
Water and sewer lines separated 6 ft horizontally and 2 ft vertically
Figure 16 : Engineering Detail 9-01-010 Underground Utilities in Streets Typical Location and Trench Detail [7]

## Slide 24: Preliminary Cost Estimate
Table 3: Cost Estimate Breakdown for Development of Infrastructure

## Slide 25: CONCLUSION AND RECOMMENDATIONS
Challenges
  Topography
  Sewer Trenching/ Possible need for lift station
  Large amounts of cut and export of rock
  Permitting and Plan Review Challenges
  Value Engineering Recommendations
  Master Meters vs. Individually Metered
  Residential Local Road vs. Residential Wide Road
  Decomposed Granite Walkways

## Slide 26
Figure 17: Original Gantt Chart Schedule for the Tiny Home Affordable Housing [1].

## Slide 27
Figure 3: Updated Gantt Chart Schedule for the Tiny Home Affordable Housing [1].

## Slide 28: STAFFING
SENG | ENG | EIT | INT
Senior Engineer | Engineer | Engineer in Training | Intern
Table 4: Project Member Titles and Abbreviations for staffing of the Affordable Housing Tiny Home Project [1]
Table 5: Original Hours provided for each project member for each task listed [1]

## Slide 29: STAFFING
SENG | ENG | EIT | INT
Senior Engineer | Engineer | Engineer in Training | Intern
Table 6: Project Member Titles and Abbreviations for staffing of the Affordable Housing Tiny Home Project [1]
Table 7: Updated Hours provided for each project member for each task listed [1]

## Slide 30: COST OF ENGINEERING SERVICES
Table 8: Cost of Engineering Services Breakdown for Personnel and Travel on the Tiny Home Affordable Housing Site Design [1]
Table 9: Cost of Engineering Services Breakdown for Personnel and Travel on the Tiny Home Affordable Housing Site Design [1]

## Slide 31: REFERENCES
[1] Habitat for Humanity Tiny Homes Affordable Housing Site Design Proposal for Flagstaff Unified School District in Flagstaff, Arizona. ABK : Anna Kurn, David Borja, Michael Bulriss, Abdulrahim Abdullah, Mobarak Alsulaiman. CENE 476 Capstone : https://onedrive.live.com/view.aspx?resid=565C70869A7714A1!116&ithint=file%2cdocx&app=Word&authkey=!AmFru8ZQYdBNQkQ
[2] Karl Eberhard, Tiny Home Designs. https://karleberhard.com/multifamily/#/habitat-soliere/
[3] Habitat for Humanity Tiny Homes Affordable Housing Site Design Proposal for Flagstaff Unified School District in Flagstaff, Arizona. Anna Kurn, David Borja, Michael Bulriss, Abdulrahim Abdullah. CENE 486 Capstone: Report. Available: https://nau0-my.sharepoint.com/:w:/r/personal/alk299_nau_edu/_layouts/15/Doc.aspx?sourcedoc=%7B7764cc5e-9fbb-4301-8510-6df88ffef1f1%7D&action=default&gad=2574
[4] City of Flagstaff, "Title 10: Flagstaff Zoning Code," 24 January 2019. [Online]. Available:
https://www.codepublishing.com/AZ/Flagstaff/.
[5] City of Flagstaff, “Stormwater Management Design Manual – City of Flagstaff” Created March 2009. [Online]. Accessed March 2019. Available: https://www.flagstaff.az.gov/DocumentCenter/View/58133/SWMgmtDesignManual-3-09?bidId=
[6] City of Flagstaff, “Sparrow Ave Record Drawings FINAL”. September 18th, 2018. Print.
[7] “Engineering Detail 9-01-010: Underground Utilities in Streets Typical Location and Trench Detail,” City of Flagstaff Engineering Standards. [Online]. Available: https://www.flagstaff.az.gov/DocumentCenter/View/14939/Title-23-APPENDIX-A---STANDARD-DRAWINGS?bidId=. [Accessed: 05-Mar-2019].

## Slide 32: QUESTIONS?