## Slide 1: SAE AERO
Chase Beatty (Team Leader)
Brian Martinez (Organizer)
Mohammed Ramadan (Financial Officer)
Noe Caro (Historian)
Chase Beatty

## Slide 2: CUSTOMER description
Dr. John Tester
  SAE advisor since 2000
Judges at AERO competition
Academic advisor
  Dr. Tom Acker
Chase Beatty

## Slide 3: Society of Automotive Engineers
Student engineering club
Annual SAE Aero competition west
Aero capstone project since 2009
Competing in regular class
Choose as senior design project
Chase Beatty

## Slide 4: Project description
Design and build an airplane
Combined dimensions cannot exceed 225”
Take off within 200ft
Land and stop within 400ft
Payload and airplane cannot exceed 55lbs
Fly in a circle at least once
No lighter than air aircrafts or helicopters
Land Land within 400’ 0’
Takeoff within 200’
Brian Martinez

## Slide 5: Project description cont.
Propeller cannot be made out of metal
Fiber-Reinforced Plastic is prohibited
No fuel pump
Cannot used gear boxes—gear ratio
Fuel supplied by competition
No gyroscope
Brian Martinez

## Slide 6: Airfoil Key Parameters
  CL – Lift Coefficient , Cd – Drag Coefficient , Stall , α – Angle of Attack (AoA)
  Lift to Drag Ratio
Mohammed Ramadan
Stall: is a sudden drop in the lift coefficient when reaching a critical AoA

## Slide 7: Airfoil Analysis
(Lift Coefficient vs AoA)
Mohammed Ramadan
Profili
E 423
Max Cl = 1.89 at 12
Stall beginning at12
Clark Y
Max Cl = 1.39 at 12
Stall around 12 to 15

## Slide 8: Airfoil Analysis CONT.
Mohammed Ramadan
(Drag Coefficient vs AoA)
E 423
Cd= 0.035 at 12
Cd = 0.02 at 9
Clark Y
Cd= 0.030 at 12
Cd = 0.015 at 9
Profili

## Slide 9: Airfoil Analysis CONT.
(Lift to Drag Ratio vs AoA)
Mohammed Ramadan
Profili
E 423
L/D max = 97 at 6°
Clark Y
L/D max = 79 at 6°
Maximum L/D is an
important parameter
in airfoil performance
efficiency

## Slide 10: Airfoil Design
Mohammed Ramadan
SolidWorks & Profili
4 lightening holes
3 spar locations
Initial chord = 13 inches
Max thickness = 1.63 inches

## Slide 11: Horizontal Tail section
An Aspect Ratio of 4 will be used for the horizontal tail section
  This horizontal span will be about 32 in with a chord of 9 in
There will be no taper in the horizontal tail
Equations:
Planform Area
Horizontal Span
Horizontal Chord
(Anderson)
Noe Caro

## Slide 12: Vertical tail section
Aspect Ratio will be 1.5
The vertical tail will be tapered at a ratio of 50%
Will have a root chord of 11.75 in
Will have a tip chord of 4.5 in
Will have a span of 14 in
Equations:
Planform Area
Vertical height on tail section
Root chord
Tip chord
Noe Caro

## Slide 13: Final Design
Noe Caro

## Slide 14: Takeoff and landing calculations
)
= Takeoff Velocity
= Stall Velocity
= Landing Distance
= Touchdown Velocity
W = Weight
  ρ = Air Density
  A = Constant
  B = Constant
We calculated our design to take-off within 200 ft with a 22 lb payload
Chase Beatty

## Slide 15: Wing Structural Analysis
22 lb loading with ends of the wings fixed
Maximum Stress- 2600 psi
Maximum displacement- 1.1 in
Yield Stress of balsa-3000 psi
Chase Beatty

## Slide 16: Deliverables
Constructed airplane
Competition
Final Report
Brian Martinez

## Slide 17: Budget
 | Estimated Budget (dollars)
Registration | 600
Fuel Cost (Transportation) | 450
Hotel Cost (4 nights) | 300
Food/Drink Cost | 600
Balsa Wood | 30
Bass Wood | 20
Monokote | 30
O.S. 61FX | 150
Servos | 50
Receiver | 100
TOTAL | 2330
Brian Martinez
 | Updated Budget (dollars)
Registration | 600
Fuel Cost (Transportation) | 450
Hotel Cost (3 nights) | 327
Food/Drink Cost | 600
Balsa Wood | 117.40
Bass Wood | 5.80
Monokote | 30
O.S. 61FX | 0
Servos | 176.95
Receiver | 0
TOTAL | 2307.15

## Slide 18: Current Stage of Construction
Noe Caro

## Slide 19: Project Schedule
Finish Servo connection and placement (3/3)
Monokote Aircraft (3/3)
Complete web page (4/24)
Finish poster (4/26)
Finish final report (5/4)
Noe Caro

## Slide 20: Conclusion
Finish airplane electronics
Finish making payload
Construct back up set of wings
Test airplane in flight by certified pilot Fred (3/10)
Competition (3/16-3/18)
Noe Caro