## Slide 1: LABORATORY FUME HOOD SUMMER 2020 TEAM 5
Shirley Hatcher
Bryce Davis
Zachary Bell
Talal Alshammari

## Slide 2: PROJECT DESCRIPTION
Client - Dr. Zachary Lerner
Project Sponsor - Dr. Lerner with the NAU Biomechatronics Laboratory
Primary Objective - Create safe environment when working with carbon fiber
Requirements - Compatible with EBR 50 Exhauster
Additions - Filter Capacity Monitor and Display
Figure 1: EBR 50 Exhauster fan

## Slide 3: DESIGN DESCRIPTION
The current design state has been focused on the housing for the electronics to protect them
This functions by keeping the electronics in a closed container with cutouts to allow for access to connections on the arduino board.
Fume hood design for ease of assembly and manufacturing has been found and the models are still being worked on.

## Slide 4
Design Description
Figure 2: Arduino Housing Front view
Figure 2: Arduino Housing iso view

## Slide 5: Design Description
Figure 2: Arduino Housing board view

## Slide 6: ENGINEERING REQUIREMENTS AND ACTION ITEMS
Dimensions – (4x3x2 feet) – Target in progress- waiting on confirmation
Weight – Combined weight < 80lbs. - Target met
Volumetric flow rate – 395 Cfms - Target Met exhauster operates at 395 cfm
Air flow velocity- 4,000 fpm – Target met due to fan standards
Pressure drops – maintain < 2 kPa – In Progress
Maneuverability – Portability – Target Met
Shell durability – At minimum 200 Kpsi
Filter assessment time – 5 seconds – In Progress
Fan compatibility – Compatible with Ebr 50 Fan – target met
Capture efficiency/cleaning percent – Retain >80% of particulates- In progress

## Slide 7: ENGINEERING REQUIREMENTS AND ACTION ITEMS Bill of Materials
We are waiting for design approval from Dr. Lerner on a specific fume hood design.
Depending on design chosen we will be able to implement a proper bill of materials for the project. Until we receive concrete confirmation we implemented our proposed materials for the pressure system.
Bill of Materials |  |  | 
Part | Cost | quantity | Source
Arduino starter kit | 91.90 | 1 | https://store.arduino.cc/usa/arduino-starter-kit
LCD Shield kit | $19.95 | 1 | https://www.adafruit.com/product/772
4” O.D. air filter | $6.68 | 1 | https://www.homedepot.com/p/ProTeam-Dome-Filter-with-Foam-Media-for-ProTeam-Triangular-Vacs-510183/206454327
3-D printed housing | $5-10 | 1 | 
Pressure sensor | $15 | 1 | Donated through NAU
Arduino Starter Kit: Necessary Components | 
Component | Quantity
Arduino Uno board | 1
400- Point bread board | 1
Jumper wires | 2
Phototransistor | 1
Temperature Sensor | 1
LED Lights | 3
Resistors | 3
Table 2: Arduino system Components
Table 1: Arduino system BOM

## Slide 8: ENGINEERING REQUIREMENTS AND ACTION ITEMS Completed Action items
Talal
Gannt Chart
Implementation plans for our 3 proposed options
Zach
Arduino housing 3-D Cad Model
Compilation of manufacturing process 2: injection molding through NAU
Manufacturing process research
Bryce
Compilation of manufacturing process 3: pre-manufactured fume hood
6” to 4” reducer 3-D Cad model
Filter Assessment research and analysis
Shirley
Pressure differential system research
Compilation of manufacturing process 1: modified polyethylene box
Research and analysis of testing plan for Arduino and pressure systems.

## Slide 9: MANUFACTURING AND ASSEMBLY Option 1: Modified Polyethylene Bin
Total Manufacturing Cost = $549.98
Pros:
· The design is based around client feedback
· Cost effective
· Exceptionally durable and portable
Cons:
· The manufacturing and assembly
· Less elegant design
· No physical testing on Prototype
Figure 2: Fume Hood Structure
Figure 3: Polycarbonate Sheeting
Figure 4: Fume Hood Bin Lid

## Slide 10: MANUFACTURING AND ASSEMBLY
Option 2
The manufacturing of the fume hood would be done using resources through NAU to minimize costs.
The manufactured design would be split into 3 seperate systems as to ensure easy manufacturing and assembly.
The 3 systems would be the top pyramidal roof section, the central walls with user access port, and the bottom structural base.

## Slide 11: MANUFACTURING AND ASSEMBLY Pre-purchased fume hood
Pre-Manufactured Fume hood from Belart: $1289.55
Pros:
Meets dimensions : 42x20x30”
Large sash opening 34.5x14”
One piece molded fume hood
Lightweight (56 lbs.)
Made from polyethylene plastic- durable and resistive to the corrosiveness of carbon fiber
Rounded pyramidal shape which fits with the team specifications and designs. This shape also reduces the risk of eddies, re-circulation zones, and dead spots within the hood
Figure 5: Large Molded fume hood from Belart

## Slide 12: MANUFACTURING AND ASSEMBLY Pre-purchased fume hood
Pre-Manufactured Fume hood from Belart: $1289.55
Cons:
Price points 3x the budget ($400)
Cfm capability difference, our fan runs at 395 cfms while the recommended cfms for this hood is 350 cfms
Stack is 6” which is too big for the exhauster fan, a 3-D printed reducer would need to be manufactured. Pictured in figure 2
Figure 6: Necessary 3-D printed reducer for hose and stack

## Slide 13: IMPLEMENTATION PLAN
Table 3: Gantt Chart.

## Slide 14: IMPLEMENTATION PLAN For Option 1
If Dr. Lerner approved the option of modified polyethylene bin, the team will provide a design manual that includes:
Poly Box Truck dimensions and specifications
Lid dimensions and specifications
Polycarbonate sheets dimensions.
Modification manual
Assembly manual
Differential pressure system codes and manual.
Filter specification
Cost Analysis

## Slide 15: IMPLEMENTATION PLAN For Option 2
If Dr. Lerner approved the option of manufacturing the fume hood according to the team’s design, the team will provide a design manual that includes:
Fume hood dimensions.
Materials specifications
Differential pressure system codes and manual.
Assembly Plans
Filter specifications
Cost Analysis

## Slide 16: IMPLEMENTATION PLAN For Option 3
If Dr. Lerner approved the option of Pre-Purchasing the fume hood, the team will provide a design manual that includes:
Fume Hood cost analysis
Fume hood purchasing sources
Fume hood Modifications
Fume hood assembly manual
Filter specification
Differential pressure system codes and manual
Cost Analysis

## Slide 17: TESTING PLAN
Colored Smoke and Fine Wood Chips
Velocity Probe borrowed from Dr.Baxter
Extra Fine Filter Pads
Theoretical Mathematical Modeling
Figure 6 : Flow Demonstration