## Slide 1: NG Super Sonic Rocket
Presenters: Austin Paothatat, Avery Charley, Koi Quiver,
Lindsey Dineyazhe

## Slide 2: Project Description
Our team is building a two-stage supersonic rocket out of Carbon Fiber Materials. The goal is to meet a set of advanced requirements no other Capstone Team. These include an altitude of 40,000ft, a sustained speed of Mach 2, and hold a 10 lb. payload. The budget for this project is $7,000 and the team expects to use every dollar to achieve this goal.
Stakeholders
  Northrop Grumman
Austin 9/26/24 NG Super Sonic Rocket

## Slide 3: CAD: Nose Cone
Lindsey 4/1/24 NG Super Sonic Rocket
Notes: Nose cone helps to reduce aerodynamic drag, control, and stability which helps with speed, acceleration, altitude, and fuel usage.

## Slide 4: CAD: Fins
Lindsey 4/1/24 NG Super Sonic Rocket
Notes: Controls direction and stability, also helps with speed, acceleration, and altitude.

## Slide 5: CAD: 2nd Stage Assembly
Koi 4/1/24 NG Super Sonic Rocket

## Slide 6: CAD: 2nd Stage Assembly
Koi 4/1/24 NG Super Sonic Rocket

## Slide 7: CAD: Sep System
Avery 4/1/24 NG Super Sonic Rocket
Separation system is now a protected design under Northrop Grumman Space Systems, Launch Vehicles Division.
No technical data, visuals or prototypes will be displayed or discussed for the remainder of the project.

## Slide 8: CAD: Motor Mount
Austin 4/1/24 NG Super Sonic Rocket

## Slide 9: CAD: Avionics
Austin 4/1/24 NG Super Sonic Rocket

## Slide 10: CAD: Full Launch Vehicle
Austin 4/1/24 NG Super Sonic Rocket

## Slide 11: CAD: Full Launch Vehicle
Austin 4/1/24 NG Super Sonic Rocket

## Slide 12: Design Requirements ER and CR
Koi 4/1/24 NG Super Sonic Rocket
ER Description/Goals Ranks:
  Vehicle Speed – Mach 2.0 or
  Vehicle Acceleration – 12 g's
  Payload Weight – 10 lbs
  Separation Event – Successful or Not
  Body Material - 45lbs
  Altitude – 40000 ft
  Body Diameter – Inner dia. 6.00 in
  Reusable – 5 uses
  Payload volume – 282.7 in^3
CR Description Ranks:
  Max Velocity – Set a goal
  Altitude – Set a goal
  Separation Event – Specific Separation Method
  Payload Weight – Specific goal
  Lightweight – General Goal
  Cost of Production – General Goal
  Reusable – General Goal
  Payload Volume – Not set
*The client would like the design in US English units.

## Slide 13: Design Requirements QFD
Koi 4/1/24 NG Super Sonic Rocket
Discussions with Client changed the weights and rankings of CR's.
Changed the weights of ER's.
Re-weighted the body rankings
ER Importance:
  Vehicle Speed
  Vehicle Acceleration
  Payload Weight
  Separation Event
  Body Material
  Altitude
  Body Diameter
  Reusable
  Payload volume

## Slide 14: Engineering Calculations: Sep. System
Conditions of Separation
  Altitude = 9500 ft
  Velocity = 430mph (630.67ft/s)
Holding Strength:
  10.12lbf * 6 = 60.72lbf ≥ W1 = 13.01lbf
Assisted Separation Strength:
  F = -kx = -1.9lbf/in(-4.658in) 8.85lbf
  Number of Springs (6)  53.1lbf
Avery 4/1/24 NG Super Sonic Rocket
W = 48.53lbf
FD = 60.18lbf
Ff = 1586.81lbf
W = 13.01lbf
Ff = 857.76lbf
Upper Stage
Lower Stage
Sep. System

## Slide 15: Engineering Calculations: Nosecone
Lindsey 4/1/24 NG Super Sonic Rocket
387 K
γ = 1.4
Ma = 2
Fineness Ratio
Stagnation Temperature
Typical cure temperatures for carbon fiber pre-pregs ~ 250 °F or 350 °F, therefore a resin system that is cured at 350 °F would be preferred

## Slide 16: Engineering Calculations: Rocksim
Austin 4/1/24 NG Super Sonic Rocket

## Slide 17: Engineering Calculations: Fin Drag
Koi 4/1/24 NG Super Sonic Rocket
Used the Drag Force formula:​
​
​
​
Variables:​
C_d = 0.005​
V = Mach 2 = 1535 (mph) = 686 (m/s)​
A = 26 (in^2) = 0.103226 (m^2)​
P = 8.80349*10^-2 (kg/m^3) = 0.0880349 (kg/m^3)​
​
Answer:​
D = 10.7 N = 2.403 (lbf) (Individual fin)​
D_tot = 10.7 N * 8 = 85.53 (N) = 19.23 (lbf) (total of all fins)​
​
Assumptions: Coefficient is of a flat plate at turbulent flow, the density of air is at an elevation of 20,000ft, the area used is the planform area. Some error due to compressiblility at Mach 2.​

## Slide 18: Failure Mode Element Analysis
Avery 4/1/24 NG Super Sonic Rocket
Item # | Item | Failure | Root Cause | Likelihood 1 = least 5 = most | Severity 1 = least 5 = most | Precaution | Performance 1 = least 5 = most | Schedule 1 = least 5 = most | Cost 1 = least 5 = most
1.1 | Separation System (Staging) | Fails to Separate, buckling, thermal, | Electrical Failure, Mechanical failure | 3 | 5 | Ground Testing before launch to certify system | 1 | 3 | 3
1.2 | Separation System (Structural) | Failure in flight of sep. system, impact, thermal | System detaches mid-flight/ aero forces exceed limits | 2 | 4 | Ensure system is secured before flight. | 1 | 3 | 3
1.4 | Body (Structural) | Body bending, cracks, deformities | Forces during flight/temperature | 2 | 5 | Visual/NDT inspections | 2 | 2 | 3
1.5 | Fins (Structural) | Bending, cracks, deformities | Material deformation, adhesive epoxy failure | 2 | 5 | Visual/ NDT inspections | 2 | 2 | 3
1.6 | Avionics | Flight computers do not set off energetics | Battery failure, electrical short, match failure | 2 | 5 | Ground testing with energetics | 4 | 2 | 3

## Slide 19: Testing Procedures
Austin 4/1/24 NG Super Sonic Rocket
Structural Component Testing: Composite material strength testing, Separation system, Fin assembly.
  These components will be simulated and tested to ASME D638 and other applicable standards.
  Meets our structural testing requirement
Functionality Test of Systems: Avionics deployment, Separation system deployment, Payload ground testing
  All systems will be tested individually for this series of tests.
  Proves function of systems apart of the staging system and payload
Systems Test: Full dress rehearsal of the launch vehicle (Not including energetics)
  Proves launch vehicle is ready for flight and functions as expected
Subscale Testing: Built and tested subscale launch vehicle
  Further proves components and will be used for scale up data collection and improvements. This will be launched to collected data.
Full scale launch: Final launch vehicle will be constructed and ran through the testing procedures and complete a full flight.

## Slide 20: Budget Plans
PHOTO
Lindsey 4/1/24 NG Super Sonic Rocket
Funding:
1) Northrop Grumman - $7,000
2) Fundraising 10% - $700
  GoFundMe - $160
  Friends/Family Donations
  Potential fundraising collaboration w/Rocket Club
  In-contact with Nova Kinetics for material donations
  Lead with McMaster-Carr for hardware donations
  Donations from other organizations suggested by client
Budget | Description | Amount
Funding Available | Northrop Grumman | $7,000
Pending Expenses | Sep system parts | ~$60
Anticipated Expenses | Avionics, RockSim Licenses, Rocket motor propellant, Separation System parts | ~$3,000
Balance |  | $6,040

## Slide 21: Schedule (02/26-04/01)
Lindsey 4/1/24 NG Super Sonic Rocket

## Slide 22: Next Steps
Lindsey 4/1/24 NG Super Sonic Rocket
Website Update
Prototype 2
Analysis on designed components
Prototype revision and testing
Continuing fundraising and reaching out for sponsorship and donations
Planning for next semester

## Slide 23: Conclusion
PHOTO
NG Super Sonic Rocket
Thank you!
Questions?

## Slide 24: CAD: Booster Assembly
Koi 4/1/24 NG Super Sonic Rocket