## Slide 1: 33% Hardware Update
Boeing Autonomous
Elise C., Selina C., Jake K., Marek L., Desirae M., Natasa P., Lily Q.

## Slide 2: Design Efforts
Main Assembly of Go-Kart

## Slide 3: Brakes
ML & JK 3
Updates
Base plate & caliper bracket: re-manufacture for better precision & fit.
Spool: 3D metal print in progress
Exploring direct motor mounting & caliper arm actuation to drop pull-by-wire.
Calculations Changed
New bracket calculations complete: 3000 N worst-case load.
Overall FoS = 3.2 (calculated from bending in legs, bending at bolt holes, direct shear in legs, and combined weld shear; mainly affected by bending in the legs)
Exceeds target ≥2.5
Brake Assembly

## Slide 4: Brakes
ML 4
Spool
Base Plate
Brake Caliper

## Slide 5: Steering
SC 5
Updates:
Motor Mount Redesign
Gear box Manufacturing
Finalized & Attached Gears
Removed Electrical Box
Calculations:
Baseplate thickness
U Clamp thickness
Required Minimum Gear Ratio
Gear System Stress Analysis
Technical Drawing of Steering Assembly

## Slide 6: Steering
SC 6
Calculation Design Results
Baseplate thickness ~4mm minimum for aluminum
U Clamp thickness ~ 0.841mm for steel
Required Minimum Gear Ratio ~ 1:2
Gear System Stress Analysis
  Allowable Bending Stress ~ 1.644 N/mm^2 (pinion) & 12.53 N/mm^2 (gear)
  Calculated Bending Stress ~ 1.644 N/mm^2 (pinion) & 12.53 N/mm^2 (gear)
  Allowable Contact Stress ~ 14.743 N/mm^2 (pinion) & 13.458 N/mm^2 (gear)
  Calculated Contact Stress ~ 13.458 N/mm^2 (pinion) & 14.743 N/mm^2 (gear)
All calculations can be found in the appendix

## Slide 7: Steering
Gearbox Progression
SC 7
Previous Gear Box Design
Current Gear Box Design

## Slide 8: Steering
Current Gearbox Front
Current Gearbox Back
New Gearbox Drawing

## Slide 9: Steering
Motor Mount Progression
SC 8
Previous Motor Mount Design
Current Motor Mount Design

## Slide 10: Steering
Baseplate Drawing
Top Plate Drawing
Wedge Drawing

## Slide 11: Throttle
NP 9
Design Overview
Changes:
Cable
  Original Component: Cable Wire
  New Component: Bowden Cable
Assembly Location
  Original: Top Chassis
  New: Bottom Chassis
Spool
  Original: Glued Cable
  New: Cable and Shaft Held by Set Screw
Stepper Mount
  Original: (2) 8in L-Brackets
  New: (1) Welded 3in. x 3in. L-Bracket
Mechanical Driving System
  Original: Pedal with Potentiometer
  New: Hand Accelerator
Throttle Stepper Assembly

## Slide 12: Throttle
Design Evolution
NP 10
Original Stepper Design
Updated Stepper Design
Original Pedal Control Design
Updated Pedal Control Design
Original Bowden Support
Updated Bowden Support

## Slide 13: Throttle
Schematics and Calculations
New Question: Does the chosen Bowden cable offer enough tension and efficiency to safely withstand the stepper motor?
Variables: 4.55N [1] dwire = 1.5mm dcable,min = 15mm MPa [3]
Equations: [2]
Conclusion: 2.97 N/mm^2 Maximum Cable Stress, 4.5 to 5.25N Cable Tension, 0.867 Efficiency
The Bowden cable is reliable in providing enough tension and a high safety factor to pull the stepper motor.
NP 11
Throttle Stepper Assembly
Throttle Stepper Wire Spool
Throttle Stepper L-Bracket

## Slide 14: Purchasing & Manufacturing Plan

## Slide 15: Brakes
JK 13
Completed ​
Caliper mounting bracket prototype (cut, welded, milled from A36 flat bar)​
Motor Mounting Bracket prototype ​
FEA on resized spool channel
In Progress​
3D metal printing spooling components.​
Scheduled​
Motor mounting & direct caliper arm actuation (design phase, fabrication pending till February 4th)​
Base plate & bracket re-manufacturing- Feb 5th (for precision & fit)​
Spool 3D metal printing & production, targeted for, Feb 9-12th​
% Purchased | 90 %
% On-Hand | 90 %
% Manufactured | 21.90%

## Slide 16: Steering
SC 14
% Purchased | 82%
% On-Hand | 70%
% Manufactured | 11.11%
Completed ​
Gearbox
Motor Mounting prototype ​& design
Gears Finalization
In Progress​
Manufacturing motor mount
Motor Testing (Electrical)
Scheduled​
Assembling motor mount (2/9)
Finalizing fail safe mechanism design (2/13)
Complete all mechanical portions (3/16)

## Slide 17: Throttle
EC 15
Completed
L-bracket for Stepper Motor
Stepper Spool
In Progress
Mounting Acceleration Handle
Bowden Clamping Tip
Scheduled
Upgrade Throttle Lever Spring
Upgrade Base Plate and Clamps
% Purchased | 91%
% On-Hand | 82.6%
% Manufactured | 60.63%

## Slide 18: Electrical
LQ 16
% Purchased | 100 %
% On-Hand | 81%
% Manufactured | 100%
Completed
Sensor Mounting
In Progress
Hall Sensor mounting
Wiring
Scheduled
PCB soldering

## Slide 19: Budget
EC 17

## Slide 20: Demonstrations

## Slide 21: Brakes
ML 19

## Slide 22: Steering
DM 20

## Slide 23: Throttle Demo
NP 21

## Slide 24: Electrical Mounts
LiDAR Sensor
LiDAR Mount

## Slide 25: Gantt Charts

## Slide 26: Brakes
 |  |  |  |  |  |  | 12-Jan | 19-Jan | 26-Jan | 2-Feb | 9-Feb | 16-Feb | 23-Feb | 2-Mar | 9-Mar | 16-Mar | 23-Mar | 30-Mar | 6-Apr | 13-Apr | 20-Apr | 27-Apr
Task | Project Lead/s | Start Date | End Date | Days | Estimated Hours | Actual Hours | Wk 1 | Wk 2 | Wk 3 | Wk 4 | Wk 5 | Wk 6 | Wk 7 | Wk 8 | Wk 9 | Wk 10 | Wk 11 | Wk 12 | Wk 13 | Wk 14 | Wk 15 | Wk 16
Project Management | Everyone | 12-Jan | 18-Jan | 6 | 6 | 8 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
CAD Packet Rework | Jacob,Marek | 13-Jan | 20-Jan | 7 | 20 | 25 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Engineering Calculations | Jacob,Marek | 18-Jan | 25-Jan | 7 | 10 | 16 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
First Test | Everyone | 25-Jan | 9-Feb | 15 | 25 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Boeing Demo | Everyone | 10-Feb | 17-Apr | 66 | 120 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
33% Progress | Jacob,Marek | 12-Jan | 3-Feb | 22 | 30 | 34 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
67% Progress | Jacob,Marek | 12-Jan | 26-Feb | 45 | 60 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
100% Progress | Jacob,Marek | 12-Jan | 25-Mar | 72 | 90 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
ML 23

## Slide 27: Steering
 |  |  | Week |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Task | Start Date | End Date | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
Final CAD | 12-Jan | 20-Jan |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Motor Testing | 20-Jan | 30-Jan |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Gearbox Manufacturing | 20-Jan | 2-Feb |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Gear Mounting | 20-Jan | 2-Feb |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Motor Mount Manufacturing | 20-Jan | 15-Feb |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Motor and Gearbox Mounting | 15-Feb | 22-Feb |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Testing Gears with Motor | 15-Feb | 1-Mar |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Initial Testing with Entire System | 1-Mar | 15-Mar |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Finalizations | 16-Mar | 30-Mar |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
LQ 24

## Slide 28: Throttle
 |  |  |  |  |  | Week |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Throttle Subsystem | Start Date | End Date | Days | Estimated Hours | Actual Hours | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
Project Summary and Management | 12-Jan | 19-Jan | 7 | 15 | 18 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Redesign of Stepper Mount | 20-Jan | 24-Jan | 4 | 8 | 8 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Mounting Stepper Mechanism | 25-Jan | 29-Jan | 5 | 12 | 15 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Testing Stepper Mechanism (33% Progress) | 30-Jan | 01-Feb | 3 | 6 | 8 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Designing Mount for Hand Accelerator | 04-Feb | 10-Feb | 6 | 10 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Test Hand Accelerator | 12-Feb | 14-Feb | 3 | 6 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Improve Base Plate and C-Clamps for Stepper Mount | 15-Feb | 20-Feb | 5 | 14 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Improve Spring Strength in Throttle Lever (66% Progress) | 21-Feb | 24-Feb | 3 | 6 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Re-Manufacture Spool using Metal | 25-Feb | 04-Mar | 7 | 15 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Testing and Improving all Components | 16-Mar | 27-Mar | 14 | 30 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
NP 25

## Slide 29: Thank you!
Questions?

## Slide 30: References
[1] E. Oberg and C. J. Mccauley, Machinery’s handbook : a reference book for the mechanical engineer, designer, manufacturing engineer, draftsman, toolmaker, and machinist. New York: Industrial Press, 2012.
[2] J. H. Jung, N. Pan, and T. J. Kang, “Capstan equation including bending rigidity and non-linear frictional behavior,” Mechanism and Machine Theory, vol. 43, no. 6, pp. 661–675, Jun. 2008, doi: https://doi.org/10.1016/j.mechmachtheory.2007.06.002.
‌
[3] R. G. Budynas, J Keith Nisbett, and Joseph Edward Shigley, Shigley’s mechanical engineering design, 11th ed. New York, Ny: Mcgraw-Hill Education, 2020.
‌

## Slide 31: Appendix
Gear System Stress Analysis Hand Calculations
Required Gear Ratio Hand Calculations

## Slide 32: Appendix
Minimum Thickness for Plate
Minimum Thickness for U-Bracket Script

## Slide 33: Appendix